## Slide 1: The BIOWAT

## Slide 2: Problem Statement
Chart: Quantity of Biomedical waste water(liquid waste) generated(in liter) on daily basis at Nartiang PHC approximately 560 Liters
| Laundry Waste Water | Housekeeping Fluid | Others(greywater) | Disinfecting fluid | Laboratory waste water
Sales | 230 | 200 | 100 | 15 | 15

## Slide 3: (Environmental Issues)

## Slide 4: Description
BIOWAT- short for Biomedical Waste Water Treatment
An improvised facility for the treatment & disposal of liquid waste (Biomedical waste water) generated at Primary Health Center, Nartiang West Jaintia Hills Meghalaya.
At BIOWAT, following a simple primary, liquid waste undergoes four stages of treatment before disposal viz.,
Intermittent/Demand operated Slow sand filtration
Chlorine Disinfection
Carbon Adsorption
De-chlorination with Vitamin-C(ascorbic acid)

## Slide 5
SSF (Demand Operated)
Flow Meter-1
Chlorine contact Tank
GAC Bed-1
GAC Bed-2
GAC Bed-3

## Slide 6
At BIOWAT, dechlorination with Vitamin-C(ascorbic acid) is the final stage of treatment of biomedical waste water. Free residual chlorine is neutralized based upon a reaction by M.W.Tikkanen et al., in 2001.

## Slide 7: Outcome (Discharge parameters of effluent)
Free Chlorine : 0mg/L
pH: 7-7.5
Fish survival 100%>96hrs
Turbidity: < 5NTU

## Slide 8
Estimated cost:
Initial Start cost: Rs.200000/- (rupees two lac only).
Daily running (logistic support)cost:Rs.20/-(rupees twenty only)
Annual (cost of GAC): Rs.10000(rupees ten thousand only)
Partners:
Health Engineering wing

## Slide 9
Benefits:
Simple operation and maintenance
Efficient removal of chlorine
Zero energy consumption for daily operation
Low cost – start up and running
Scalability:
Health Department in the process of replication at PHCs & CHCs

## Slide 10: THANK YOU